## Slide 1
Dial Caliper
Description and Use
© 2012 Project Lead The Way, Inc.
Introduction to Engineering Design

## Slide 2: Dial Caliper
Dial Calipers are arguably the most common and versatile of all the precision measuring tools used by engineers and manufacturers

## Slide 3: Dial Caliper Measurement
Four Measurements
  Outside Diameter or Object Thickness
  Inside Diameter or Space Width
  Step Distance
  Hole Depth

## Slide 4: Dial Caliper Limit
Standard inch dial caliper will measure slightly more than 6 inches

## Slide 5: Measuring Outside Length
Measurement made between caliper faces shown
Example is outside diameter or object thickness
Outside Measuring Faces

## Slide 6: Measuring Outside Length
Example of measuring outside length of object

## Slide 7: Measuring Inside Length
Measurement made between caliper faces shown
Example is slot width or hole
Inside Measuring Faces

## Slide 8: Measuring Inside Length
Example of measuring inside diameter

## Slide 9: Measuring Stepped Length
Measurement made between caliper faces shown
Example is stepped parallel surfaces
Step Measuring Faces

## Slide 10: Measuring Stepped Length
Example of measuring step distance

## Slide 11: Measuring Depth
Measurement made between caliper faces shown
Example is depth of hole or recess
Depth Measuring Faces

## Slide 12: Measuring Depth
Example of measuring depth
  Work piece shown as section view
  Dial caliper shortened for clarity

## Slide 13: Dial Caliper Parts: Blade
Blade is the immovable portion of the dial caliper
Slider moves along blade to adjust the distance between the measuring surfaces
Slider
Blade

## Slide 14: Dial Caliper Parts: Blade
Blade scale divides each inch into 10 increments
Each increment equals one tenth of an inch (0.100 in.)

## Slide 15: Dial Caliper Parts: Dial and Pointer
Pointer rotates within the dial as the slider moves back-and-forth along the blade
Pointer
Dial

## Slide 16: Dial Caliper Parts: Reference Edge
Reference edge keeps track of larger increments (i.e., 0.100 in.) as the slider moves along the rack
Reference Edge

## Slide 17: Dial Caliper Parts: Rack
Rear-toothed rack gear is used to change linear motion (slider) to rotary motion (pointer)
Rack

## Slide 18: Dial Caliper Interpretation
Accurate dial caliper reading requires several steps

## Slide 19: Dial Caliper Interpretation: Zeroing
Before measuring, zero the caliper
  Close caliper completely
  Loosen dial lock
  Rotate dial to read zero
  Tighten dial lock
Dial Lock
Zero Alignment

## Slide 20: Dial Caliper Interpretation
Each time the pointer completes one rotation within the dial, the reference edge on the slider moves the distance of one blade scale increment (0.100 in.)

## Slide 21: Dial Caliper Interpretation
One revolution of the pointer within the dial represents one tenth of an inch (0.100 in.)
Dial is divided 100 times; therefore, each graduation equals one thousandth of an inch (0.001 in.)

## Slide 22: Dial Caliper Interpretation: Practice
To determine the outside diameter of this pipe section
  first identify how many inches are being shown on the blade scale

## Slide 23: Dial Caliper Interpretation: Practice
Reference edge is located between the 1 and 2 inch marks
Record inch significant digit
1.000 in.
1 in. Mark

## Slide 24: Dial Caliper Interpretation: Practice
Identify the 0.1″ increment marks shown to the right of the last inch mark
Record tenth inch significant digit
0.4 in. Mark
1.000 in.
0.400 in.

## Slide 25: Dial Caliper Interpretation: Practice
Identify the pointer increment mark shown on the dial
Record thousands inch significant digits
0.037 in. Mark
1.000 in.
0.400 in.
0.037 in.

## Slide 26: Dial Caliper Interpretation: Practice
Estimate the ten thousands inch significant digit
0.0001 in. estimate
1.000 in.
0.400 in.
0.037 in.
0.0001 in.

## Slide 27: Dial Caliper Interpretation: Practice
Add values together for dial caliper measurement
1.000 in.
0.400 in.
0.037 in.
1.4371 in.
+
0.0001 in.

## Slide 28: Dial Caliper Interpretation: Practice
How wide is the block?
1.000 in.
0.400 in.
0.002 in.
1.4022 in.
+
0.0002 in.

## Slide 29: Dial Caliper Interpretation: Practice
Complete Activity 3.4 Making Measurements